## Slide 1: PFC Flyback Converter
Final Presentation
Anat Rom · Shoval Buzaglo
Supervisor: Eric Herbelin · Spring 2026
Notes: Introduce the project and the team.

## Slide 2: What is a Flyback Converter?
An isolated DC-DC converter whose transformer stores energy while the switch is on and releases it to the output while it is off.
Switch ON – store
The rectified line voltage sits across the primary; its current rises linearly at Vin / Lp and energy builds up in the transformer's magnetic field. The output diode is blocked.
Switch OFF – release
The stored energy transfers to the secondary, the diode conducts, and the secondary current falls linearly into the output capacitor and load.
Notes: A flyback is a buck-boost converter with a coupled inductor. The "transformer" is really an energy store: during the on-time the primary current ramps up and energy is stored in the core; when the switch opens the energy flies back to the secondary through the diode. The winding ratio (n ≈ 2.66 in our design: Lp = 90 µH, Ls = 12.7 µH) sets the voltage conversion and the transformer provides galvanic isolation. Regulation is closed across the isolation barrier with a TL431 and a 4N25 optocoupler. In a PFC flyback the input is the rectified mains, so the input voltage itself varies as a rectified sine.

## Slide 3: Why Do We Need PFC?
Switching loads draw current in sharp peaks and distort the mains.
A PFC stage forces the input current to follow the input voltage.
A slow control loop (~10 Hz) averages the power demand; DC capacitors absorb the fast pulses.
Without PFC: current flows only at the voltage crest (PF = 0.57)
Notes: Without correction, the input current flows only in narrow pulses at the voltage crest.

## Slide 4: Project Definition & Goals
Design and verify a 12 V / 9 W PFC Flyback converter controlled by an Arduino-class microcontroller instead of a dedicated PFC chip.
Key Performance Targets:
▸ Power Factor: ≥ 0.98 resistive, > 0.95 under varying loads
▸ Low THD: mild increase under “violent” loads
▸ Current Tracking: sinusoidal, in phase with Vin
▸ Output Stability: Vout under load steps
▸ Efficiency: measured per operating point
▸ MCU Feasibility: slow loop + one timer register

## Slide 5: Project Steps
1 Theoretical Study and Requirement Definition
2 Characterization of the Reference Unit (EV44010)
3 Design of Our Arduino-Controlled Converter
4 LTspice Modelling and Simulation Campaign
5 Design of the Measurement System
6 Laboratory Measurements on the Prototype
7 Data Processing and Conclusions

## Slide 6: Conduction Modes: CCM, DCM, BCM
CCM
Current never reaches zero
+ Low peak currents
− Reverse recovery, RHP zero
DCM
Current stays at zero before next cycle
+ No reverse recovery, simple loop
− High peak and RMS currents
Our design
BCM
Switch turns on exactly at zero current
+ Soft turn-on, Ipk = 2·Iavg
− Variable frequency, harder EMI filter
Reference unit

## Slide 7: Reference Unit: EV44010 Flyback
EV44010-S+4688-N-01A board
Simplified PFC Flyback power stage

## Slide 8: EV44010 Flyback Simulations
Reference unit, constant 0.359 A output current – load level set by the output resistance
Static loads – power factor
Load | R | R + L series | R ∥ L
100 % | 0.988 | 0.989 | 0.937
75 % | 0.992 | 0.994 | 0.933
50 % | 0.986 | 0.990 | 0.926
25 % | 0.961 | 0.982 | 0.905
η at 100 % | 85.8 % | 85.8 % | 61.5 %
▸ R and R + L: PF ≥ 0.96 at every load level
▸ R ∥ L: PF 0.91–0.94, efficiency only 54–61 %
Pulsed load – PF range vs. pulse rate
■ 50 → 100 % step ■ 25 → 75 % step bar = min to max PF
Notes: Simulation results of the reference unit (EV44010). The unit drives a constant 0.359 A output current, so the load level is set by the output resistance: 122 Ω (100 %), 92 Ω (75 %), 61 Ω (50 %), 30.5 Ω (25 %). The inductive cases use L = 4.076 H with 20.4 Ω winding resistance. Static loads: with a resistor, or a resistor with the inductor in series, the PF stays at 0.96–0.99 at every level, and efficiency is about 86 % at full load, falling to 72–78 % at quarter load. With the inductor in parallel with the resistor, the PF drops to 0.91–0.94 and efficiency to 54–61 %. Pulsed load (50 % duty): at pulse rates of 25 Hz and above the PF stays between 0.97 and 0.99, and moves by no more than 0.005 inside a run. At 10 Hz and below, which is close to the ~10 Hz bandwidth of the voltage loop, the loop starts following the load and the PF swings widely: down to 0.59 (50→100 %) and 0.41 (25→75 %). The efficiencies above 100 % logged for the 10 Hz and 5 Hz pulse runs are measurement artefacts and are not shown.

## Slide 9: MP44010 Controller – BCM Control
▸ On-time: multiplier sets a sinusoidal peak-current envelope
▸ Off-time: ZCS pin detects zero current and restarts the cycle
▸ Result: average current in phase with Vin → PF ≈ 1
▸ Protection: two-stage OVP, zero-crossing compensation, starter

## Slide 10: Our Design: Arduino-Controlled Flyback
Specification
Input: 35.36 V RMS (50 V peak), 50 Hz
Output: 12 V / 9 W, isolated
Switching: fixed 100 kHz, DCM
Feedback: TL431 + 4N25 optocoupler
Controller: Arduino-class MCU
No PFC → PFC: Four Changes
Bulk capacitor removed: Cin 125 µF → 10 nF
Slow feedback: 100 kΩ / 150 nF, fc ≈ 10.6 Hz
Control variable: on-time instead of duty cycle
Protection: cycle-by-cycle limit at 2.6 A

## Slide 11: Reference Unit vs. Our Design
We keep the core idea of the EV44010 – a slow voltage loop commanding a constant on-time – and drop the parts an MCU cannot run at switching speed.
Function | EV44010 / MP44010 (reference) | Our Arduino design
Conduction mode | BCM, variable frequency | DCM, fixed 100 kHz
Voltage loop | Error amplifier, bandwidth below ~10 Hz | Slow loop, fc ≈ 10.6 Hz (kept)
Current shaping | Multiplier sets a sinusoidal peak envelope | Constant on-time – the transformer multiplies
Cycle restart | ZCS pin on an auxiliary winding | MCU timer, every 10 µs
Peak current | Ipk = 2·Iavg | 1.95 A peak for 0.7 A output
Protection | Two-stage OVP, zero-crossing comp., starter | Cycle-by-cycle limit at 2.6 A
Notes: This slide summarises what we took from the reference unit and what we replaced. Kept: a slow voltage loop (below ~10 Hz) that commands a constant on-time. Dropped: the multiplier, the zero-current detector and the auxiliary winding, none of which a microcontroller can support at switching speed. The price is DCM's higher peak and RMS currents (1.95 A peak primary current for 0.7 A output) – acceptable at 9 W.

## Slide 12: Digital Constant On-Time Control
A fixed on-time makes the transformer do the multiplication: the averaged input current follows Vin(t) with no fast current loop.
⟨iin⟩ = Vin(t) · Ton² / (2 · Lp · Ts)
≈ 153 Ω
Emulated resistance Re
3.43 µs
Average on-time command
0.08 %
On-time variation over line cycle

## Slide 13: LTspice Models
Without PFC
Duty-cycle PI regulator, Cin = 125 µF

## Slide 14: LTspice Models
With PFC
Slow loop → constant Ton, Cin = 10 nF

## Slide 15: Switching Regime Verification – DCM
fs = 100 kHz, traces: V(pwm), I(Schottky), V(drain)
Without PFC
Dead time + free ringing, ~5 A diode peaks
With PFC (line crest)
Constant 3.43 µs on-time, ~5 µs demagnetisation

## Slide 16: Without PFC vs. With PFC
Vin = 35.36 V RMS, Vout = 12 V, resistive load ≈ 9 W, window 0.46–0.50 s
0.5698
PF
139.8 %
THD
80.1 %
η
0.9976
PF
6.95 %
THD
85.1 %
η

## Slide 17: PFC – Inductive and Capacitive Loads
Same output power (≈ 8.3 W), only the load character changes
Inductive
PF 0.9975
THD 7.01 %
Capacitive
PF 0.9975
THD 6.97 %

## Slide 18: Load Character Comparison
Case | PF | THD [%] | Irms [A] | Pout [W] | η [%]
No PFC (reference) | 0.5698 | 139.77 | 0.562 | 9.08 | 80.13
PFC – Resistive | 0.9976 | 6.95 | 0.278 | 8.33 | 85.12
PFC – Inductive | 0.9975 | 7.01 | 0.275 | 8.24 | 85.07
PFC – Capacitive | 0.9975 | 6.97 | 0.275 | 8.30 | 85.59
PF varies by only 0.01 % between load types – the hypothesis holds for static loads.

## Slide 19: Time-Varying Load – Repeated Steps
Fixed load character, increasing step magnitude, window 0.46–0.50 s
50 → 100 %
PF 0.9962
100 → 150 %
PF 0.9966
100 → 200 %
PF 0.9918
100 → 400 %
PF 0.8846

## Slide 20: Load Step Comparison
Load Step | PF | THD [%] | Pout [W] | Vout min / max [V] | η [%]
50 → 100 % | 0.9962 | 8.66 | 5.18 | 11.61 / 12.69 | 83.53
100 → 150 % | 0.9966 | 8.20 | 10.31 | 11.34 / 12.97 | 85.33
100 → 200 % | 0.9918 | 12.50 | 10.23 | 11.07 / 13.10 | 85.02
100 → 400 % | 0.8846 | 49.12 | 13.26 | 10.52 / 13.34 | 83.70
▸ Up to 2× step: PF > 0.99
▸ At 4×: DC-bus energy runs out – displacement factor still ≥ 0.9997

## Slide 21: Future Implementation Steps
▸ Build the hardware prototype and reproduce the static cases
▸ Sweep load steps between 2× and 4× to find the PF = 0.95 point
▸ Measure output-voltage recovery time after a single step
▸ Repeat the 4× case with added bulk capacitance
▸ Compare against a BCM variant with zero-current detection

## Slide 22: Conclusion
▸ Digital PFC on an Arduino-class MCU works: PF 0.57 → 0.998, THD 140 % → 7 %
▸ PF is independent of load character (R, L, C all ≈ 0.9975)
▸ PF depends on load dynamics – limited by DC-bus energy storage
▸ All PF loss is harmonic distortion; phase shift never exceeds 1.3°
▸ Average Vout within 0.2 % of 12 V in every case